Specification

Product:		24” Deep x 36” Wide General purpose downdraft table

Application:	Non-Powered Down Draft table complete with integrated collection area and 3' X 5' work surface. Draws contaminants away from workers’ breathing zone without hindering movement.

Revision:		March 30, 2009

1.	DT-23 (www.LEV-CO.com)

1.1.	General:

1.1.1.	The following down draft table shall be of industrial quality, and be designed to be used for direct source capture of pollutants through the table top by down-drafting. They shall be manufactured to withstand the environments associated with these applications and shall remove the pollutants in accordance with all industrial ventilation guidelines.

1.2.	Construction:

    - Non-Powered Down Draft table complete with integrated collection area and 3' X 5' work surface. Draws contaminants away from workers’ breathing zone without hindering movement

1.2.2.	14 gauge welded zinc coated steel cabinet, finished with a two part chemical and oil

resistant paint.

1.2.3.	Includes a heavy duty steel grate, a 10” diameter ring on back wall of unit for ducting, and a 6” deep removable dust tray.

1.3.	 Specification:

1.3.1.	STD DIM: 36.50" W x 25" D x 29" H [0.93m W x 0.64m D x .74m H]

1.3.2.	WEIGHT: 180 lb. (STD) [82 kg]

1.4	Options:

1.4.1	DT23-ALUM	Aluminum Grate Option for Standard DT-35 Unit

1.4.2	DT23-BF1	12" High Back Fence Kit Option for Standard DT-23 Unit

1.4.3.	DT23-BF1-AL	12" high aluminum back fence

1.4.4.	DT23-BF3	Enclosed 36" Tall Fence Kit Option for Standard DT-23 Unit

1.4.5.	DT23-COATED	Vinyl Coated Grate Option for Standard DT-23 Unit

1.4.6.	DT23-FIBER	Fiberglass Grate Option for Standard DT-23 Unit