Specification

Product:		BI Direct Drive - Self Cleaning Wheels - Inverter Duty - (1,000 - 21,000 CFM)

Application:	Centrifugal direct-drive exhaust fans for industrial applications.

Revision:		May 11, 2010

1.	(1,000-2,000 CFM) (2,000-4,000 CFM) (3,000-6,000 CFM) BI Direct Drive - Self Cleaning Wheels - Inverter Duty - (1,000 - 21,000 CFM) (www.LEV-CO.com)

1.1.	General:

1.1.1.	The following units shall be of industrial quality, and be designed to be used for exhaust of industrial applications. They shall be manufactured to withstand the environments associated with these applications and when the appropriate local extraction devices are selected, these fans shall remove the pollutants in accordance with all industrial ventilation guidelines.

1.2.	 Construction:

    - Direct Drive Fans, Arr. #4 c/w punched flanged outlet, slip fit inlet, motor, motor mounting support and drain. Motors are TEFC E-Pact 230-460V/575-600V/3/60/-3500 RPM. Wheels are heavy gauge, single thickness, backward inclined, dynamically balanced to ANSI S2.19-1989 specifications for smooth operation.

1.2.2.	NB: All Lev-Co LD fans come in a standard configuration of Clockwise rotation / Up-blast discharge. For alternate rotations and discharges, please indicate on your purchase order and approved submittal drawings

1.3.	Specifications:

1.3.1.	Flow rate: Models available form 1,000 to 21,000 CFM

1.3.2.	Lower initial cost plus lower maintenance cost (no v-belt drives, fan shaft or bearings to replace).

1.4.	 Options

1.4.1. Inlet Collar

1.4.2. Inlet Flange

1.4.3. Inlet Vane Control

1.4.4. Drain

1.4.5. Inlet and Outlet Guards

1.4.6. Inspection Door

1.4.7. Outlet damper

1.4.8. Shaft Seal

1.5.	Performance ratings

1.5.1	See Spec Drawing for performance curves