Product:	Fume Booth 800

Application:	Bench top paint booths for odours & VOC’s (volatile organic compounds) for use in a non-sparking & flameless environment.

VOC’s suited to this application include: paint thinners, solvents, semiconductor cleaner, and some constituents of petroleum fuels.

##### Specification:

- Portable, self-contained unit: Easy to set up and use anywhere; includes 5” diameter heavy duty casters for added maneuverability.

- Heavy-duty top mounted table with 150 PSF rated Aluminum grate: Provides maximum loading of up to 275 lbs.

- High efficiency 2-stage filtration: Provides up to 95% filtration efficiency

- Direct-drive blower: Higher static pressure, longer filter life and greater reliability; non-sparking; no belts or pulleys to replace.

- Ultra-Seal® filter mounting: Eliminates contaminant bypass of filters.

- Removable doors: Easy access for cleaning and filter changeout.

- Prewired to explosion proof box: Meets Group-D electrical requirements.

##### Options :

- Pressure Gauge Kit: Indicates when filters require cleaning.

- 95% Main Filter and Double Adsorption Modules

- Motor Starters/Disconnects

- Plastic Coated Grate

##### Construction :

- Construction: 16 ga. steel, powder coated cabinet

- Blower Pkgs (HP): 1.5

- Noise Level (dBA): 72

- Electrical: Group-D 1.5 HP - 115/208-230/1/60, 17.0/8.5 amps,

##### Dimensions

- Width: 32.00”

- Height: 76.00”

- Depth: 25.00”